SNMP exercises

AfNOG 11, Kigali

Please run all exercises on your assigned router:

Row 1: 196.200.218.249

Row 2: 196.200.218.250

Row 3: 196.200.218.251

Row 4: 196.200.218.252

Row 5: 196.200.218.253

- Make sure that snmp commands work

  - snmpstatus -v1 -c afnog 196.200.218.254

  - What do you see?

  - Does v2c, v3 also work? Why, why not?

  - Does it also work to your local machine? Why, why not?

- Do an SNMP GET request

  - snmpget -v2c -c afnog 196.200.218.254 sysUpTime.0

  - Why do you need the .0?

  - easier: snmpwalk -v2c -c afnog 196.200.218.254 sysUpTime

- Browse a MIB file

  - MIBs are installed under: /usr/share/snmp/mibs

  - Look at /usr/share/snmp/mibs/RFC1213-MIB.txt

  - Try to read the hierarchy and find the OID for sysUpTime Hint: mib-2 is .1.3.6.1.2.1

  - Verify: snmpwalk -v2c -c afnog 196.200.218.254 <yourOID>

  - If you want to get the results without name resolution do
snmpwalk -v2c -On -c afnog 196.200.218.1 <yourOID>
or if you want the full name hierarchy use -Of

- Find some information

  - What is the location of the router in your workgroup (196.200.218.249/250/251/252/253 for row 1/2/3/4/5)? Hint: Check in the system tree

  - What is the MAC address of FastEthernet0/1 on this router? Hint: Get the whole interface table and try to read it - it’s a table by ifIndex - find the ifIndex for FastEthernet0/1 and find the MAC address for this interface

  - What’s the IP address for this interface? Get ipAdEntIfIndex from the ip tree

- Add a custom MIB

  - Run the following command:
snmpwalk -Of -v2c -c afnog 196.200.218.254 .1.3.6.1.4.1.9.9.13.1.3

  - What do you notice?

  - To insert Cisco-specific MIB information, you need to download a MIB file and put it in your path. scp them from the NOC server
As root:
cd /usr/share/snmp/mibs
wget http://noc/files/CISCO-SMI.my
wget http://noc/files/CISCO-ENVMON-MIB.my

  - Add variables so it can find the mibs 
export MIBDIRS=/usr/share/snmp/mibs 
export MIBS=ALL

  - Try the snmpwalk command again - what is different now?

    - Note: You can find MIBs on the vendor website or FTP server usually, e.g. Cisco MIBs are in ftp://ftp.cisco.com/pub/mibs/v2/ - to see what information you can get via SNMP in addition to the standard you can read through the MIB files or vendor doc